## Slide 1: The Edge Negotiator
Verified-Source Cross-Junction Coordination for SLM-Driven Traffic Signal Control
UCL MSc Systems Engineering for IoT — Project Proposal & Status
Student 25153651 · Supervisors: Dr Akin Delibasi (UCL), Lee Stott (Microsoft)
Small language-model agents that coordinate traffic lights, verify who they talk to,
and catch faulty/spoofed data — evaluated in SUMO on a real London corridor.

## Slide 2: What we're building & why
Problem: traffic signals decide blind to neighbours; multi-agent coordination needs trustworthy data.
Per-junction SLM agents (Phi-4-mini via Microsoft Foundry Local) coordinate signal timing in Eclipse SUMO.
Deterministic MaxPressure shield validates / overrides every SLM decision — safety first.
Cryptographic agent identity (Ed25519 + on-chain permissioned registry) — verify the source.
Vehicle-conservation check flags spoofed / faulty neighbour reports; tamper-evident audit log.
Novelty (integrative): authenticated identity + conservation check beneath SLM cross-junction coordination — no published precedent.

## Slide 3: Current status — built & validated
Scope pivoted & locked (supervisor-approved); single source-of-truth decision brief.
Literature base: 175 papers (incl. 28 new on agent identity & spoof / fault detection).
DONE: SUMO 2x2 grid + MaxPressure baseline — beats fixed-time (waiting 52 s vs 66 s).
DONE: SLM-in-the-loop — Phi-4-mini drives a junction live: 90 decisions, 0 failures, shield + event-gating working.
Reproducible public repo — code, scenario, docs, all committed.

## Slide 4: Next steps · what we're confident about
Next steps:
  Cross-junction coordination — share predicted neighbour state (the novel core).
  Identity + audit layer — Ed25519 signatures + Hyperledger Besu allowlist / revoke.
  Spoof / fault detection + adversarial scenarios; then real Lambeth corridor + evaluation sweep.
Confident about:
  End-to-end pipeline runs — SUMO + TraCI + SLM + shield all validated.
  Phi-4-mini serves on a consumer laptop; MaxPressure shield is provably stable.
  Identity mechanism is literature-backed and buildable within the timeline.

## Slide 5: Challenges & how we tackle them
SLM latency (Foundry serial, ~2-8 s/decision) -> terse output, pause-sim, event-gating, keep to ~6-8 SLM junctions.
Consistency check is not truth (a consistent liar evades it) -> scope to uncoordinated spoofs / faults; identity layer complements; cite the limit (Xiao 2026).
Blockchain too slow for the control loop -> async audit / registry only, never in the hot path.
Real-corridor demand data is coarse -> DfT traffic counts + SUMO routeSampler calibration.
SLM decision quality -> deterministic shield underneath; explicit-prompt engineering (already validated).