## Slide 1: The Edge Negotiator
Verified-Source Cross-Junction Coordination for SLM-Driven Traffic Signal Control
UCL MSc Systems Engineering for IoT. Project pitch.
Student 25153651, Ebenezer Veeraraju. Supervisors: Dr Akin Delibasi (UCL) and Lee Stott (Microsoft).

## Slide 2: The problem
Traffic signals act blind to their neighbours, leaving coordination gains unused.
When junctions share data to coordinate, nothing confirms that data is genuine or correct.
Signals are safety-critical infrastructure: AI control is deployable only if inputs are trusted and auditable.
Originality: securing language-model coordination with verifiable identity and a physics-based check has no published precedent.

## Slide 3: Background and the gap
Mature but separate strands: language-model traffic control, MaxPressure control, cooperative-ITS spoof and fault detection, decentralized identity and blockchain PKI, and chain-of-thought faithfulness.
Evidence base: 175 peer-reviewed sources, with 28 added for agent identity and spoof or fault detection.
The gap: nobody places authenticated identity and a vehicle-conservation check beneath language-model cross-junction coordination.
Research question: can authenticated, plausibility-checked agents coordinate a corridor while detecting spoofed or faulty inputs?
Honest limit: a consistency-respecting attacker can evade conservation checks (Xiao, 2026), so identity is a separate layer.

## Slide 4: Methodology
Per-junction Phi-4-mini agents (Microsoft Foundry Local) coordinate signals in SUMO on a real Lambeth corridor.
A MaxPressure shield validates or overrides every decision: the model proposes, the shield disposes.
Signed messages plus a permissioned Hyperledger Besu registry verify the sender and revoke compromised junctions.
A vehicle-conservation check flags physically impossible reports; every decision is logged tamper-evidently.
The model outputs only a phase number, not reasoning, because chain-of-thought is an unfaithful explanation.

## Slide 5: Evaluation and progress so far
Baselines: fixed-time, MaxPressure, and uncoordinated versus coordinated agents.
Metrics: travel time, queue and throughput; detection precision, recall and latency; trust-layer overhead.
Rigour: pre-registered seeds, bootstrap confidence intervals, multiple-comparison correction.
Already working: MaxPressure beats fixed-time, and a live language-model junction ran 90 decisions with zero failures.
All code, scenario and documentation sit in a reproducible public repository.

## Slide 6: Roadmap, confidence, and risks
Next: cross-junction coordination, then identity and audit, then adversarial evaluation on the real corridor.
Confident: pipeline runs end to end; Phi-4-mini runs on a laptop; the shield is provably stable; identity is literature-backed.
Latency risk: terse output, pause while thinking, skip quiet junctions, cap model-controlled junctions.
Trust risk: scope claims to clumsy or faulty data; the identity layer covers deliberate attacks.
Data risk: calibrate demand from Department for Transport counts using SUMO routeSampler.